## Slide 1
Failure of Metals
Dr. J. Venkatramani
219-B
venkatramani@iiitdm.ac.in

## Slide 2
Fracture – Material Separation
Two fracture modes:
Ductile
Brittle

## Slide 3
Fracture – Material Separation
Stages of fracture
Crack nucleation
Crack propagation
Brittle
Highly ductile
Moderately ductile

## Slide 4
Fracture – Material Separation
Stages of fracture
Crack nucleation
Crack propagation
Cup – Cone fracture process involved in ductile mode of failure of metals

## Slide 5
Fractographic Studies – Ductile fracture
(a) Scanning electron fractograph showing spherical dimples characteristic of ductile fracture resulting from uniaxial tensile loads @ 3300X. (b) Scanning electron fractograph showing parabolic-shaped dimples characteristic of ductile fracture resulting from shear loading @ 5000X. (From R.W. Hertzberg, Deformation and Fracture Mechanics of Engineering Materials, 3rd edition. Copyright © 1989 by John Wiley & Sons, New York. Reprinted by permission of John Wiley & Sons, Inc.)

## Slide 6
Fractographic Studies – Brittle fracture
Arrows indicate the points of origin of the cracks. V–shaped “Chevron” markings are a typical feature of brittle fracture.

## Slide 7
Fractographic Studies – Brittle fracture
Arrow indicates the location of origin of the cracks. Fan shaped radial crack pattern is also typical feature of brittle fracture.

## Slide 8
Fractographic Studies – Brittle fracture
Brittle fracture occurs by cleavage of atomic bonds on certain specific crystallographic planes.
Transgranular – crack propagation through the grains
Intergranular – crack propagation along the grain boundaries

## Slide 9
Fractographic Studies – Brittle fracture
Brittle fracture occurs by cleavage of atomic bonds on certain specific crystallographic planes.
Transgranular – crack propagation through the grains
Intergranular – crack propagation along the grain boundaries

## Slide 10
Fracture Mechanics – Stress Intensity Factor – Fracture Toughness
σ0
σ0
Stress concentration → Stress Intensity Factor → Fracture Toughness

## Slide 11
Impact Fracture Testing
Charpy test for measuring impact energy

## Slide 12
Impact Fracture Testing
Izod test for measuring impact energy

## Slide 13
Ductile–to–Brittle Transition
Range of temperatures over which a normally ductile material behaves like a brittle material and undergoes brittle failure.
Influence of carbon content on the dependence of impact energy on temperature

## Slide 14
Fatigue Failure

## Slide 15
Fatigue Failure
Stress ratio, R = σmin/σmax.

## Slide 16
Fatigue Failure: S–N curve
Ferrous Alloys
Non – Ferrous Alloys

## Slide 17
Fatigue Failure: S–N curve – Probability of failure of materials

## Slide 18
Fatigue Failure: Mechanisms

## Slide 19
Fatigue Failure: Micrograph showing various stages of fatigue crack growth

## Slide 20
Creep Deformation and Failure
Stress–induced vacancy diffusion; grain boundary diffusion; dislocation motion; grain boundary sliding.