## Slide 1
Ceramics
Dr. J. Venkatramani
219-B
venkatramani@iiitdm.ac.in

## Slide 2
Ceramics
Inorganic and non – metallic
Compounds between metallic and non – metallic elements; ionic bonding or covalent bonding.
Name derived from the Greek word “keeramikos” meaning burnt stuff. Polymer derived Ceramics are one of the recent examples indicating this meaning.
XA and XB are electronegativities.

## Slide 3
Ceramic – Crystal structures
For ionic ceramics, crystal structures depend on
the magnitude of electrical charge on each ion
Size of the ions – Cations are smaller than Anions.

## Slide 4
Ceramic – Crystal structures
For ionic ceramics, crystal structures depend on
the magnitude of electrical charge on each ion
Size of the ions – Cations are smaller than Anions.
Ionic Radii for Several Cations and Anions
(for a Coordination Number of 6)

## Slide 5
AX Type Crystal structures
NaCl – Rock Salt:
Co–ordination number = 6

## Slide 6
AX Type Crystal structures
Cesium Chloride
Co–ordination number = 8

## Slide 7
AX Type Crystal structures
Zn – Blende Structure (ZnS) or Sphalerite
Co – ordination number = 4
S atoms at the corner and face centers, while, Zn occupies interior tetrahedral positions.

## Slide 8
AmXp Type Crystal structures
Eg: CaF2
Co – ordination number = 8

## Slide 9
AmBnXp Type Crystal structures
Eg: BaTiO3
This crystal structure is called Perovskite type.
Has good electromechanical properties – suitable for applications in piezoelectric transducers.

## Slide 10
Close – Packed Planes of Anions
Similar to metals, Ceramic materials too have close packed planes and stacking sequence.

## Slide 11
Theoretical density computation
Eg: NaCl. Required data: Atomic weights of Na and Cl are 22.99 g/mol and 35.45 g/mol. Radii of Na+ and Cl– are 0.102 nm and 0.181 nm, respectively.

## Slide 12
Silicate Ceramics
The fundamental unit of a silicate.
Structure of Cristobalite: a Crystalline polymorph of Silica
Crystalline Silica has three polymorphs:
Quartz, Cristobalite and tridymite.
Low density (2.65 g/cc) and high melting point: 17100C.

## Slide 13
Silicate Ceramics – Silica Glasses
Fused silica or vitreous silica – they are called network formers.
Used for containers, windows.
Sodium–Silicate Glass

## Slide 14
Silicate Ceramics – Other Silicates
Other Silicates:

## Slide 15
Imperfections in Ceramics

## Slide 16
Ceramic Phase Diagrams – Al2O3–Cr2O3
A binary phase diagram

## Slide 17
Mechanical Properties
Brittle Fracture of Ceramics

## Slide 18
Mechanical Properties
Brittle Fracture of Ceramics

## Slide 19
Stress – Strain Behaviour of Ceramics
Flexural test

## Slide 20
Stress – Strain Behaviour of Ceramics

## Slide 21
Mechanisms of Plastic Deformation
Crystalline Ceramics display certain amount of plasticity caused by dislocation motion, although the order of plastic strains are quite negligible.
Non – crystalline ceramics undergo plastic deformation in the form of viscous flow.
For porous ceramics,

## Slide 22
Porous Ceramics
For porous ceramics,

## Slide 23
Ceramics – Classification

## Slide 24
Glasses
CaO, Na2O, K2O and Al2O3 are known materials used for glasses, containers, windows, lens, fiberglass etc.

## Slide 25
Glass Ceramics

## Slide 26
Clay and Refractory Ceramics
Clay ceramics are of two types – Structural and Whiteware
Refractories are unreactive, inert to severe environments; can be used for thermal insulation due to high melting points

## Slide 27
Abrasives

## Slide 28
Cements
Cement, Plaster of Paris and lime.
Grinding and mixing of clay and lime bearing minerals
Heating up to 14000C
The resulting powder is ground and gypsum is added to delay the setting process.
Calcination
Clinker
Portland Cement
Preparation of Portland Cement
Hydration Reaction

## Slide 29
Advanced Ceramics
Micro–Electro Mechanical Systems (MEMS)
Rack & Pinion Arrangement–miniaturization (Image @ 100X)
Various processing techniques such as photolithography, ion implantation, etching and deposition technologies are used. Micromachining techniques are also available to manufacture such miniaturized components. Silicon is the material currently under use.
Silicon carbonitrides are being considered to be used instead of Silicon alone.

## Slide 30
Advanced Ceramics
Optical Fibers are made of high purity silica.
Ceramic ball bearings are also in use now-a-days. Silicon Nitride is the material which is replacing steel.
Optical Fiber
Hybrid Ceramic ball bearing

## Slide 31
Fabrication and Processing of Ceramics
Can we adopt casting or other forming operations for processing Ceramics?

## Slide 32
Temperature sensitive behaviour of glassy or non – crystalline materials
Glasses and Glass–Ceramics

## Slide 33
Glasses and Glass–Ceramics
Glass Forming
– Pressing, blowing, drawing and fiber forming
Glass Drawing
Glass Pressing & Blowing

## Slide 34
Making of a sheet glass

## Slide 35
Clay Products
Hydroplastic forming and Sand casting
Solid slip casting
Hydroplastic forming
Drain slip casting

## Slide 36
Powder Pressing

## Slide 37
Tape Casting